## Slide 1: ECE158A: Computer Networks
Tara Javidi
Lectures: TTH 5:00-5:30pm Center Hall 222
TAs: Mohammad Ahmadypour
Topic 1
Introduction and Overview

## Slide 2
I am grateful to many authors/instructors around the country who have shared their educational material on this topic freely available online to everyone including me and my students. In particular, the content of these slides is heavily adapted from the educational resources that are made available by Pearsons authors:
Kuros & Ross and Tannenbaum & Weatherall (if you sign in you can see the slides and a whole lot more) in conjunction with the course material of Professor Jennifer Rexford at Princeton. Note that as such the content of these slides is subject to the copyright of the above authors and instructors.

## Slide 7
Website Raconteur asked over 400 scientists, tech journalists, academics, authors and interested readers to name the greatest inventions of all time.

## Slide 8: What are the design principles that made this possible? How applicable are these to other networks such as sensor nets, IoTs, smart meters, etc?

## Slide 9: Course Organization

## Slide 10: Learning Objectives
Engineering principles of network design
  Network architecture: Internet as an example
  Simple mathematical analytic tools
    Statistical multiplexing, shortest path routing, fairness resource allocation and congestion control
Network emulations/sims (assignments only)
  Precise network analysis not possible due to scale
  Simulations and emulations are used instead
  Assignments are there for you to get familiar (not enough time/resource to build expertise)

## Slide 11: Textbooks
No required book
Books on reserve
  Communication Networks: A Concise Introduction, Jean Walrand and Shyam Parekh
  Computer Networking: A Top-Down Approach Featuring the Internet, by Kurose and Ross
  Computer Networks, by Tanenbaum

## Slide 12: Grading
4 assignments (44% total; 11% each)
  95% < 5 hours, 70% <1 days late, 50% < 2 days late
Two exams (54% total)
  Midterm on October 27th (23%)
  Final exam during exam period (31%)
Class participation (2%)
  Pre-lecture Readings
  In lecture and discussion and on Piazza

## Slide 13: Policies: Submit Your Own Work
Learning and creativity in an individual process. While thinking about a problem, discussions with friends are encouraged. However, when the time comes to write your HW or your code for your project, the work must be entirely yours.
If you have a question about the HWs and projects, you can certainly ask your friends or the TA, but do not, under any circumstances, copy another person's work.
Letting someone copy your work or using someone else's work in any form is a violation of academic integrity.

## Slide 14: What is the Internet?

## Slide 15: What is the Internet?
http://en.wikipedia.org/wiki/Internet

## Slide 16: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 17: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 18: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP

## Slide 19: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 20: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP

## Slide 21: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs

## Slide 22: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network to bring services/content close to edges

## Slide 23: What is the Internet: “nuts and bolts” view
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
billions of connected computing devices:
  hosts = end systems
  running network apps
Notes: 23

## Slide 24: “Fun” Internet-connected devices
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress

## Slide 25: Behind its success: a service view
infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 26
(Giant) Computing Platform:
Software/Hardware Architecture?
Need to provide programming interface to apps
  hooks that allow sending and receiving to Internet
  conceptualizes the network as a compute resource/hardware (memory, cpu, etc)
  has to integrate with the rest of the computer (operating system)
process: program running within a host
  within same host, two processes communicate using inter-process communication (defined by OS)
  processes in different hosts communicate by exchanging messages

## Slide 27: Socket: End Point of Communication
Sending message from one process to another
  Message must traverse the underlying network
Process sends and receives through a “socket”
  In essence, the doorway leading in/out of the house
Socket as an Application Programming Interface
  Supports the creation of network applications
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 28: Delivering the Data: Division of Labor
Network
  Deliver data packet to the destination host
  Based on the destination IP address
Operating system
  Deliver data to the destination socket
  Based on the destination port number (e.g., 80)
Application
  Read data from and write data to the socket
  Interpret the data (e.g., render a Web page)

## Slide 29: Socket Identification
Communication Requirement
  streaming, reliable
  best effort, unreliable
Receiving host
  Destination address that uniquely identifies the host
  An IP address is a 32-bit quantity
Receiving socket
  Host may be running many different processes
  Destination port that uniquely identifies the socket
  A port number is a 16-bit quantity

## Slide 30: Communication Requirements for an App
Data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
Security
encryption, data integrity, …

## Slide 31: Historically Only Two Types of Services
Datagram Socket (UDP)
  Collection of messages
  Best effort
  Connectionless
Stream Socket (TCP)
  Stream of bytes
  Reliable
  Connection-oriented

## Slide 32: Socket Identification (practically)
TCP/UDP
IP
Ethernet Adapter
Process
A
Process
B
port X
port Y
Host Address
Protocol
Port Number

## Slide 33: Creating a network app
Requires writing programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
applications on hosts allow for rapid app development, propagation
Handle processes accessing ports:
socket programming
NOT the focus of this course!
used to monitor packets
Software for network core devices (SDN)
network-core devices do not run user applications
Legacy core devices are often not programmable
programmable core enables networking innovation => need for programmable routers
NOT the focus of this course; but an exciting area of reserch

## Slide 34
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received

## Slide 35: Circuit vs Packet Switching
Internet Architecture

## Slide 36: How to structure a network?
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 37: Internet: A Brief History
Maps from http://www.vox.com/a/internet-maps
1970: ARPANET expands
1973: ARPANET goes international
1984: ARPANET becomes Internet
1963: ARPANET

## Slide 38: Internet: A Brief History
1994: Privatization backbone
2012: Broadband penetration
1992: NSFNET (backbone)
1993: The internet is global

## Slide 39: Properties of Links
Capacity: “width” of the link
  number of bits sent (or received) per unit time (bits/sec or bps)
Latency (delay): “length” of the link
  propagation time for data to travel along the link (seconds)
Link rate: Peak achievable rates in practice
Capacity
Latency
Total bits in link
A
B

## Slide 40: Example of Communication Media
Unshielded Twisted Pair (UTP)
  Medium used in telephone line
  Seven categories of increasing quality
  Data rates from 0.1Mbps (CAT1) to 600Mbps (CAT6)
Coaxial cable
  Audio/TV connectors
  More resilient to external disturbances than UTP but more expensive, short distances
  Data rates up to hundreds of Mbps
Fiber optic cable
  Internet backbones
  No external disturbance, small and inexpensive
  Difficult interconnections, limited curvature
  Data rates up to 10Gbps

## Slide 41: Examples of Capacity-Delay
Propagation speed varies on the material, but it is roughly between 0.5 to 0.8 times the speed of light c, i.e., ~ 1.5x108 msec
Same city over UTP:
  Capacity~100Mbps
  Latency~0.1msec (~15Km)
  Total bits in link ~ 10,000bits ~ 1.25KBytes
Cross-country over fiber optic cable:
  Capacity~10Gbps
  Latency~10msec (~1500Km)
  Total bits in link ~ 108bits ~ 12.5GBytes

## Slide 42: Internet Submarines Cables
More maps at http://www.submarinecablemap.com/

## Slide 43: Internet Submarine cables
https://www.youtube.com/watch?feature=player_embedded&v=1ex7uTQf4bQ

## Slide 44: Packet Delay Sending a 100B packet from A to B?
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
Packet Delay = Transmission Delay + Propagation Delay
Packet Delay =
(Packet Size ÷ Link Capacity) + Link Latency

## Slide 45: Packet Delay Sending a 100B packet from A to B?
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 46: Packet Delay: The “pipe” view Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 47: What if we have more nodes?
One link for every node?
Need a scalable way to interconnect nodes

## Slide 48: Switching Network
Notes: multiple conversations in parallel
resources are shared

## Slide 49: Solution: A switched network
Nodes share network link resources
How is this sharing implemented?
Notes: multiple conversations in parallel
resources are shared

## Slide 50: Circuit switching
(1) Node A sends a reservation request
(2) Interior switches establish a connection -- i.e., “circuit”
(3) A starts sending data
(4) A sends a “teardown circuit” message
Idea: source reserves network capacity along a path
A
B
10Mb/s?
10Mb/s?
10Mb/s?
Notes: multiple conversations in parallel
resources are shared

## Slide 51: Circuit Switching: Sharing a Link
Time-division
  Each circuit allocated certain time slots
Frequency-division
  Each circuit allocated certain frequencies
time
frequency
time

## Slide 52: Time-Division Multiplexing
Time divided into frames; frames into slots
Relative slot position inside a frame determines to which conversation data belongs
  e.g., slot 0 belongs to orange conversation
Slots are reserved (released) during circuit setup (teardown)
If a conversation does not use its circuit capacity is lost!
Frames
0
1
2
3
4
5
0
1
2
3
4
5
Slots =

## Slide 53: Timing in Circuit Switching
time

## Slide 54: Timing in Circuit Switching
time

## Slide 55: Timing in Circuit Switching
time

## Slide 56: Timing in Circuit Switching
time

## Slide 57: Timing in Circuit Switching
Circuit Establishment
time

## Slide 58: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
time

## Slide 59: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 60: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons

## Slide 61: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 62: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons
  wastes capacity if traffic is “bursty”

## Slide 63: Timing in Circuit Switching
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 64: Timing in Circuit Switching
Information
Circuit Establishment
Circuit Teardown
time
Data transfer
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 65: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes capacity if traffic is “bursty”
  connection setup time is overhead

## Slide 66: Circuit switching
A
B
Circuit switching doesn’t “route around trouble”
Notes: multiple conversations in parallel
resources are shared

## Slide 67: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes capacity if traffic is “bursty”
  connection setup time is overhead
  recovery from failure is slow

## Slide 68: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes capacity if traffic is “bursty”
  connection setup adds delay
  recovery from failure is slow
  [in the telephone network] designed for a specific app

## Slide 69: Packet switching

## Slide 70: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
  Data is sent as chunks of formatted bits (Packets)
  Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
  no notion of packets belonging to a “circuit”
No link resources are reserved in advance. Instead packet switching leverages statistical multiplexing
01000111100010101001110100011001
Header
Data
header
payload

## Slide 71: Inventors of Packet Switching
Donald Davies
Leonard Kleinrock
Paul Baran
Watch the following interview with Prof. Kleinrock for a historical perspective:
https://www.youtube.com/watch?v=qsgrtrwydjw

## Slide 72: Timing in Packet Switching
time
payload
hdr
What about the time to process the packet at the switch?
We’ll assume it’s relatively negligible (mostly true)
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 73: Timing in Packet Switching
time
payload
hdr
Could the switch start transmitting as soon as it has processed the header?
Yes! This would be called a “cut through” switch
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 74: Timing in Packet Switching
time
payload
hdr
We will always assume a switch processes/forwards a packet after it has received it entirely. This is called “store and forward” switching
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 75: Statistical Multiplexing

## Slide 76: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 77: When Each Flow Gets 1/3rd of Capacity
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Frequent Overloading

## Slide 78: When Flows Share Total Capacity
Time
Time
Time
No Overloading
Statistical multiplexing relies on the assumption
that not all flows burst at the same time.
Very similar to insurance, and has same failure case

## Slide 79: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 80: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 81: Three Flows with Bursty Traffic
Data Rate 1+2+3 >> Capacity
Time
Time
Capacity
What do we do under overload?

## Slide 82: Statistical multiplexing: pipe view
time 
BW 
pkt tx time

## Slide 83: Statistical multiplexing: pipe view

## Slide 84: Statistical multiplexing: pipe view
No Overload!

## Slide 85: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 86: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 87: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 88: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 89: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Queue

## Slide 90: Statistical multiplexing: pipe view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts!

## Slide 91: Statistical multiplexing: pipe view
What about persistent overload?
Will eventually drop packets

## Slide 92: Queues introduce queuing delays
Recall, packet delay = tx delay + prop delay
With queues (stat. muxing)
  packet delay = tx delay + prop delay + queuing delay
Queuing delay caused by “packet interference”
Made worse at high load
  less “idle time” to absorb bursts
  think about traffic jams at rush hour

## Slide 93: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes capacity if traffic is “bursty”
  connection setup adds delay
  recovery from failure is slow

## Slide 94: Packet switching: pros and cons
Cons
  no guaranteed performance
  header overhead per packet
  queues and queuing delays
Pros
  efficient use of capacity (stat. muxing)
  no overhead due to connection setup
  resilient -- can `route around trouble’

## Slide 95: The Internet Protocol Stack?
Internet Architecture

## Slide 96: Protocol Layers as an Architecture
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium

## Slide 97: Protocol Layers: An Example
Example: the philosopher-translator-secretary architecture
Each protocol at different layers serves a different purpose

## Slide 98: Service Primitives (1)
A service is provided to the layer above as primitives
Hypothetical example of service primitives that may provide a reliable byte stream (connection-oriented) service:

## Slide 99: Service Primitives (2)
Hypothetical example of how these primitives may be used for a client-server interaction
Client
Server
LISTEN (0)
ACCEPT
RECEIVE
SEND (4)
DISCONNECT (6)
CONNECT (1)
SEND
RECEIVE
DISCONNECT (5)
Connect request
Accept response
Request for data
Reply
Disconnect
Disconnect
(2)
(3)
Notes: The primitives are called at the client and server by the higher layer using the service. The layer implements the primitives by sending messages using the services of the lower layer; these messages are assumed to be reliable for simplicity and the lower layer service is not otherwise described.
This is similar to the way that simple Web browsers and Web servers work today.

## Slide 100: Relationship of Services to Protocols
Recap:
  A layer provides a service to the one above [vertical]
  A layer talks to its peer using a protocol [horizontal]

## Slide 101: Protocol Layers as an Architecture
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium
This view assumes a network consists of hosts only.
Reasons to build infra-structure (simpler nodes than full fledge hosts)…

## Slide 102: Switching Network
Notes: multiple conversations in parallel
resources are shared

## Slide 103: Routers Forward Packets
Routers determine the next hop for a packet based on the destination IP address
Routing algorithms ensure packets follow the shortest path from source to destination
Each router constantly update a routing table specifying the next hop for each destination address
Destination | Next Hop
169.229.60.1 | 4
16.129.123.1 | 5
169.229.60.32 | 2
110.19.116.102 | 3
to 169.229.60.32
Routing Table
switch#2
switch#3
111010010
169.229.60.32
switch#5
switch#4

## Slide 104: Open System Interconnection (OSI)
Conceptual model of the International Organization for Standardization (ISO)
Each layer accomplishes different tasks
Well defined interfaces across layers
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 105: Open System Interconnection (OSI)
Lower two layers implemented in all network devices (routers have 3 layers, switches 2)
Top two layers implemented only at hosts
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 106: Protocol Layer: Encapsulation
Each lower layer adds its own header (with control information) to the message to transmit and removes it on receive
Layers split and join messages, etc.
Common case: 20 bytes TCP header + 20 bytes IP header + 14 bytes Ethernet header = 54 bytes overhead

## Slide 107: Example: HTTP Connection
107
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 108: Layers/Encapsulation in HTTP
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B
Link hardware
Host-to-host
connectivity
App-to-app
channels
Application

## Slide 109: Internet Protocol Layers
application layer
transport layer (TCP/UDP)
network layer (IP)
link layer (e.g. ethernet)
application layer
transport layer (TCP/UDP)
network layer (IP)
link layer (e.g. ethernet)
User Process
User Process
Socket
Socket
Internet

## Slide 110
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
End Host vs. Core (Switch vs. Router)
Ht
Hn
Hl
M

## Slide 111
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Switch vs. Router
Switch and Router have similar functionality:
  Redirecting packets from input to output (lookup table)
  Complexity grows with size
Switches are designed for local and small-scale operation (link layer)
Routers are designed to handle large scales (network layer)
EXCEPTION: multilayer (l3) switch

## Slide 112: Error, Flow, and Congestion Control
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
Digital data is translated into electronic/optical signals and transmitted
This is the job of physical layer --below link layer– and mostly beyond the scope of 158A (ECE154/157 series, ECE159)