## Slide 1: ECE158A: Computer Networks
Tara Javidi
Lectures: TTH 5:00-5:30pm Center Hall 222
Topic 7
Queuing Theory: Link-Layer Analytic Framework

## Slide 2: Packet Switching and Forwarding
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”
If we can write on egress N times faster than the ingress/egress line rate we can allow simultaneous access by queuing packets at the output

## Slide 3: Output Queueing
Packets from multiple inputs can be written on a single output
  Queued to resolve the read conflict
Conceptually simple
“Write” is often done in hardware via crossbar (for speed)
  Expensive to switch N times faster (esp for large N)

## Slide 4: Input Queueing
Packets are queued at each input
Conceptually simple
If used w FCFS, then low utilization due to HoL blocking
  Can cause throughput to be limited to 58.6%
one packet time later: green packet experiences HOL blocking
switch
fabric
output port contention:
only one red datagram can be transferred. lower red packet is blocked

## Slide 5: Virtual Output Queueing
Packets are sorted at each input based on their destination port
  Resolves the head of line blocking problem
  Constrained queuing
VoQs hold packets but only can be served
  If VOQij served, VOQij’ or VOQi’j cannot
  Scheduling = matching
Many good matches, what is the impact on delay (buffer state)?
Scheduling Matrix

## Slide 6: A Simple Queuing System
Service
Arrival Rate (
Average Number
in Queue (Lq )
Avg Time in System (W )
Avg Number in System (L )
Average Wait
in Queue (Wq )
Rate (
Departure

## Slide 7: Basic Terminology
Queuing system
  Data network where packets arrive, wait in various queues, receive service at various points, and exit after some time
Arrival rate
  Long-term number of arrivals per unit time
Occupancy
  Number of packets in the system (averaged over a long time)
Time in the system (delay)
  Time from packet entry to exit (averaged over many packets)

## Slide 8
Components of a Basic Queuing Process
Packet Types
Queue
Service Mechanism
Input Source
The Queuing System
Jobs
Arrival Process
Configuration
of Queue(s)
Queue Discipline
(order of service)
Served Jobs
Service Process
leave the system

## Slide 9: 1. The Packet Types
Population of packets and their size characteristics
The size can be fixed or varying (random)
  The latter is most common
Can be
  Homogeneous: Only one type of packets (easiest to handle)
  Heterogeneous: Several different kinds of packets

## Slide 10: 2. Arrival Process
In what pattern do packets arrive to the queueing system?
  Distribution of arrival times?
  Batch arrivals?
  Finite many packets?
  Finite queue length?
Memoryless arrival process often assumed
  First order approximation for Many real-world arrival processes which do not have heavy dependency across time

## Slide 11: 3. Service Process
How long does it take to transfer/communicate packets?
  Distribution of service times?
  Retransmission (fully or incremental redundancy)?
  Hardware/service breakdown?
Memoryless service times is a good start
  Works well for wireless channels with short memory (and not too long-term dependence)

## Slide 12: 4. Number of Servers
How many service lines are available?
Single Server Queue
Multiple Server Queue

## Slide 13
Example – Two Queue Configurations
Servers
Multiple Queues
Servers
Single Queue

## Slide 14: 5. Queue Discipline
How are packets selected from the queue for service?
  First Come First Served (FCFS)
  Shortest Processing Time (SPT)
  Earliest Due Date (EDD)
  Priority (jobs are in different priority classes)
FCFS default assumption for most systems

## Slide 15: Discrete Time M/M/1 Queue
At any given time slot a packet arrives with probability 
At any given time slot a packet/flow/file is successfully transmitted with probability 
Independent and identical across time
Assume a finite buffer size B

## Slide 16: M/M/1 Analysis

## Slide 17: M/M/1 Analysis

## Slide 18: M/M/1 Analysis

## Slide 19: M/G/1 Queue
Packet arrivals are memoryless with rate 
A packet/file/flow takes a random transmission time with CDF FT(t):= Prob (T ≤ t)
Independent and identical across time
Infinite buffer
Mean Waiting Time

## Slide 20: M/G/1 Queue
Mean Queue Length
Interesting Observations:
  Waiting time decreases if you receive smaller packets w transmit time = T/2 at higher arrival rate of
  Producing less variable packet sizes is beneficial!
    Size-based queuing to differentiate between packets/files is beneficial

## Slide 21: Back to Virtual Output Queueing
Packets are sorted at each input based on their destination port
  Resolves the head of line blocking problem
  Constrained queuing
VoQs hold packets but only can be served
  If VOQij served, VOQij’ or VOQi’j cannot
  Scheduling = matching
Many good matches, what is the impact on delay (buffer state)?
Scheduling Matrix

## Slide 22: Scheduling Matrix
VoQs hold packets but only can be served
  If VOQij served, VOQij’ or VOQi’j cannot
Allowable Schedule, S=[sij], must satisfy:
Permutation Matrix
Scheduling Matrix
(matching)
Need to expand the single queue analysis
dimensional chain to track # of packets
in each VOQ!
Departures from each queue is dependent
on departure from others (why?how?)

## Slide 23: Permutation Matrices
matrix satisfies:
Properties:
  How many distinct permutation matrices are there?
  Multiplying a matrix by a permutation matrix?
  Averaging permutation matrices and doubly sub-stochastic matrices?

## Slide 24: Permutation Matrices
matrix satisfies:
doubly sub-stochastic matrix B satisfies:
FACT: For all then is a doubly sub-stochastic matrix

## Slide 25: Scheduling Matrix
VoQs hold packets but only can be served
  If VOQij served, VOQij’ or VOQi’j cannot
Allowable Schedule, S=[sij], must satisfy:
Permutation Matrix
Scheduling Matrix
Need to expand the single queue analysis
dimensional chain to track # of packets
in each VOQ!
Departures from each queue is dependent
on departure from others (why?how?)

## Slide 26: General Formalism
Scheduling Matrix
Need to expand the single queue analysis
dimensional chain to track # of packets
in each VOQ!
Departures from each queue is dependent
on departure from others (why?how?)
  are (random) matrices
  Simplest case: independent arrivals to VOQij w prob
Need to expand the notion of stochastic process to track dimensional random matrices!

## Slide 27: Solution Methodologies
Analytical results (formulas)
  Pros: Quick answers, insight
  Cons: Often inaccurate or inapplicable
Explicit simulation
  Pros: Accurate and realistic models, broad applicability
  Cons: Can be slow
Hybrid simulation
  Intermediate solution approach
  Combines advantages and disadvantages of analysis and simulation
Original content: D. Bertsekas, MIT

## Slide 28: Randomized Scheduling
Scheduling Matrix
  (random) matrix of 0s and 1s independent arrivals to VOQij w prob
  (random) permutation matrix selected randomly
Need to expand the notion of stochastic process to track dimensional random matrices!

## Slide 29: Analysis

## Slide 30: Analysis

## Slide 31: Randomized Scheduling
Scheduling Matrix
  (random) matrix of 0s and 1s
  independent arrivals to VOQij w prob
  (random) permutation matrix selected randomly
  Conclusions:
  To ensure stability:
  If service rate falls below , we are in trouble!! so to just ensure stability of VOQs, we need the knowledge of !

## Slide 32: Stable Scheduling
Scheduling Matrix
  (random) matrix of 0s and 1s
  independent arrivals to VOQij w prob
  permutation matrix selected based on the state of the switch (which VOQ gets priority
  Challenges:
  Adaptive to traffic variations
  Low complexity
  Fairness

## Slide 33: Maximal Scheduling
Scheduling Matrix
  (random) matrix of 0s and 1s
  independent arrivals to VOQij w prob
  permutation matrix selected to serve maximum number of packets (maximal matching)
    Complexity?
  Seminal Work (Dai and Prabhakar, 2000):
   Not sufficient for all loads
   Sufficient if
Or equivalently switch speed up of 2 