## Slide 1: ECE158A: Computer Networks
Tara Javidi
TTH 5:00-6:30pm Center Hall 222
Topic 2
Layered Architecture
&
Protocol Stack

## Slide 2
I am grateful to many authors/instructors around the country who have shared their educational material on this topic freely available online to everyone including me and my students. In particular, the content of these slides is heavily adapted from the educational resources that are made available by Pearsons authors:
Kuros & Ross and Tannenbaum & Weatherall (if you sign in you can see the slides and a whole lot more) in conjunction with the course material of Professor Jennifer Rexford at Princeton. Note that as such the content of these slides is subject to the copyright of the above authors and instructors.

## Slide 3
Internet: “network of networks”
  Interconnected ISPs
  Programmable: allows for nodes dynamically joining and departing
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What is the Internet?
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 4: Architecture Driven by Scale
Networks can be classified by their scale:
Scale | Type
Vicinity | PAN (Personal Area Network) »
Building | LAN (Local Area Network) »
City | MAN (Metropolitan Area Network) »
Country | WAN (Wide Area Network) »
Planet | The Internet (network of all networks)
Notes: An “internetwork” is any larger network made up of smaller component networks. The “Internet” (with a capital I) is the set of all connected networks.

## Slide 5: Personal Area Network
Connect devices over the range of a person
Example of a Bluetooth (wireless) PAN:

## Slide 6: Local Area Networks
Connect devices in a home or office building
Called enterprise network in a company
Wireless LAN
with 802.11
Wired LAN with
switched Ethernet

## Slide 7: Metropolitan Area Networks
Connect devices over a metropolitan area
Example MAN based on cable TV:
Notes: This is a common way in which home subscribers obtain access to the Internet in the US.

## Slide 8: Wide Area Networks (1)
Connect devices over a country
Example WAN connecting three branch offices:
Notes: The company probably leases the transmission lines (since most companies do not have their own lines).

## Slide 9: Wide Area Networks (2)
An ISP (Internet Service Provider) can be a WAN.
Customers buy connectivity from the ISP
Notes: Now the company/customer buys service from an ISP who uses its own lines to deliver packets.

## Slide 10
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network (MAN)
global ISP
regional ISP
home
network
(LAN)
Institutional
network
(LANs)
Architecture Driven by Scale

## Slide 11: Network Architcture
Last lecture we saw the division of labor among the application layer, operating system, and network layer allows for innovation in developing apps
We also saw the relationship between socket programming, network access (ports), networking APIs
Historically the development of sockets and the packetization give rise to an architecture

## Slide 12: Giving rise to an architecture…
TCP/UDP
IP
Network Interface
Process
A
Process
B
port X
port Y
Host Address
Required Service
Port Number

## Slide 13: Socket and Process Communication
The interface that the OS provides to its networking subsystem naturally creates an architecture
application layer
transport layer (TCP/UDP)
network layer (IP)
link layer (e.g. ethernet)
application layer
transport layer (TCP/UDP)
network layer (IP)
link layer (e.g. ethernet)
OS network
stack
User Process
User Process
Socket
OS network
stack
Socket
Internet
Internet
Internet

## Slide 14: The Internet Protocol Stack?
Internet Architecture

## Slide 15: Protocol Layers as an Architecture
Protocol layering is the main structuring method used to divide up network functionality.
Each protocol instance talks virtually to its peer
Each layer communicates only by using the one below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 16: The Physical Layer
Foundation on which other layers build
  Properties of wires, fiber, wireless limit what the network can do
Key problem is to send (digital) bits using only (analog) signals
  Done through line coding, pulse shaping, and modulation
Physical
Link
Network
Transport
Application

## Slide 17: PHY Layer Functionalities/Header
PHY layer functionalities (services) depend strongly on transmission technology
  Synchronization per frame (preamble)
  Bit-by-bit or symbol-by-symbol delivery over a standardized interface
    Modulation and Line Coding: representing the digital signal by a waveform optimally tuned to the technology
    Equalization, pulse shaping, forward error correction
Main task:
  Transmitter a packet (binary sequence) into a waveform over the medium
  Receiver reconstructs the transmitted packet

## Slide 18: Theoretical Basis for Point-Point Data Communication
Fundamental limits on the rate of reliable communication
  Nyquist Rate »
  Bandwidth-limited signals »
  Maximum data rate of a channel »
  Eg. additive white Guassian noise (AWGN)
Max. data rate = B log2(1 + S/N) bits/sec

## Slide 19: Example PHY technologies
Media have different properties, hence performance
  Wires:
    Twisted pairs »
    Coaxial cable »
    Power lines »
  Fiber cables »
  Wireless
  Reality check
    Storage media »
Property | Wires | Fiber
Distance | Short (100s of m) | Long (tens of km)
Bandwidth | Moderate | Very High
Cost | Inexpensive | Less cheap
Convenience | Easy to use | Less easy
Security | Easy to tap | Hard to tap

## Slide 20: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
2G: IS-95, CDMA, GSM
2.5G: UMTS/WCDMA, CDMA2000
802.15
802.11b
802.11a,g
3G: UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
4G: LTWE WIMAX
802.11a,g point-to-point
450
802.11n
Data rate (Mbps)
1300
802.11 ac

## Slide 21: Reality Check: Storage media
Send data on tape / disk / DVD for a high bandwidth link
  Mail one box with 1000 800GB tapes (6400 Tbit)
  Takes one day to send (86,400 secs)
  Data rate is 70 Gbps.
Data rate is faster than long-distance networks!
But, the message delay is very poor

## Slide 22: Beyond Maximum Rate
Throughput: File size B transferred over T seconds results in throughput B/T bps
  Not the same as link rate
  Accounts for protocol issues, etc
Delay: the time interval between arrival and delivery (we will analyze later)
Jitter: Delay rarely the same for every packet of the file but a random variable; Jitter is maximum variation in delay