## Slide 1: ECE158A: Computer Networks
Tara Javidi
Lectures: TTH 5:00-5:30pm Center Hall 222
Topic 3
Link Layer

## Slide 2: The Data Link Layer
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data (Link Layer)
  Handles sharing the local communication link (Medium Access Control)
Physical
Link
Network
Transport
Application

## Slide 3: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 4: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide reliable over link
transportation analogy:
trip from La Jolla to Bristol
  limo: La Jolla to SAN
  plane: SAN to LHR
  train: LHR to Bristol
tourist = datagram
Each transport segment = communication link
travel mode (tickets, check-in, boarding) = link layer protocol
planner/admin = routing algorithm

## Slide 5: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical

## Slide 6: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 7: Adaptors communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 8: Possible Services
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11
Acknowledged connection-oriented service
  Connection is set up; rare
Half-duplex and full-duplex
  Nodes at both ends of link can(not) transmit simultaneously

## Slide 9: Link layer services (I)
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
    only 6 bytes
reliable delivery between adjacent nodes
  seldom needed on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    We will see link-level is in addition to end-end reliability?

## Slide 10: Link layer services (II)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission

## Slide 11: Framing Methods
  Byte count »
  Flag bytes with byte stuffing »
  Flag bits with bit stuffing »
  Physical layer coding violations
    Use non-data symbol to indicate frame

## Slide 12: Framing – Byte count
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case

## Slide 13: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!

## Slide 14: Framing – Bit stuffing
Stuffing done at the bit level:
  Frame flag has six consecutive 1s (not shown)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted
Transmitted bits
with stuffing
Data bits

## Slide 15: Flow Control
Prevents a fast sender from out-pacing a slow receiver
  Receiver gives feedback on the data it can accept
  Rate in the Link layer as NICs run at “wire speed”
    Receiver can take data as fast as it can be sent
Flow control is a service provided by the Link and Transport layers
Notes: We’ll get to this later in the chapter (sliding window protocol) but note that flow control is mostly the responsibility of the Transport layer in practice (e.g., TCP)

## Slide 16: Line Cards (Interface Cards, Adaptors)
Packet handling
  Packet forwarding
  Buffer management
  Link scheduling
  Packet filtering
  Rate limiting
  Packet marking
  Measurement
to/from link
to/from switch
lookup
Receive
Transmit
Receive incoming packet from link input interface
Lookup packet destination port in forwarding table
Validate checksum, decrement ttl, update checksum
Buffer packet in input queue
Send packet to output interface (interfaces?)
Buffer packet in output queue
Send packet to output interface link

## Slide 17: Queue Management Issues
Scheduling discipline
  Which packet to send?
  Some notion of fairness? Priority?
Drop policy
  When should you discard a packet?
  Which packet to discard?
Goal: balance throughput and delay
  Huge buffers minimize drops, but add to queuing delay (thus higher RTT, longer slow start, …)

## Slide 18: Examples: FIFO Scheduling & Drop-Tail
Access to the bandwidth: first-in first-out queue
  Packets only differentiated when they arrive
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet
✗

## Slide 19: A Simple Queuing System
Service
Arrival Rate (
Average Number
in Queue (Lq )
Avg Time in System (W )
Avg Number in System (L )
Average Wait
in Queue (Wq )
Rate (()
Departure

## Slide 20: Basic Terminology
Queuing system
  Data network where packets arrive, wait in various queues, receive service at various points, and exit after some time
Arrival rate
  Long-term number of arrivals per unit time
Occupancy
  Number of packets in the system (averaged over a long time)
Time in the system (delay)
  Time from packet entry to exit (averaged over many packets)

## Slide 21
Components of a Basic Queuing Process
Packet Types
Queue
Service Mechanism
Input Source
The Queuing System
Jobs
Arrival Process
Configuration
of Queue(s)
Queue Discipline
(order of service)
Served Jobs
Service Process
leave the system

## Slide 22: 1. The Packet Types
Population of packets and their size characteristics
The size can be fixed or varying (random)
  The latter is most common
Can be
  Homogeneous: Only one type of packets (easiest to handle)
  Heterogeneous: Several different kinds of packets

## Slide 23: 2. Arrival Process
In what pattern do packets arrive to the queueing system?
  Distribution of arrival times?
  Batch arrivals?
  Finite many packets?
  Finite queue length?
Memoryless arrival process often assumed
  First order approximation for Many real-world arrival processes which do not have heavy dependency across time

## Slide 24: 3. Service Process
How long does it take to transfer/communicate packets?
  Distribution of service times?
  Retransmission (fully or incremental redundancy)?
  Hardware/service breakdown?
Memoryless service times is a good start
  Works well for wireless channels with short memory (and not too long-term dependence)

## Slide 25: 4. Number of Servers
How many service lines are available?
Single Server Queue
Multiple Server Queue

## Slide 26
Example – Two Queue Configurations
Servers
Multiple Queues
Servers
Single Queue

## Slide 27: 5. Queue Discipline
How are packets selected from the queue for service?
  First Come First Served (FCFS)
  Shortest Processing Time (SPT)
  Earliest Due Date (EDD)
  Priority (jobs are in different priority classes)
FCFS default assumption for most systems

## Slide 28: Performance Metrics
  Admission Control and Service Disciplines
  Delay
  Delay variation (jitter)
  Packet loss
  Efficient sharing of bandwidth
  Relative importance depends on traffic type (audio/video, file transfer, interactive)
  Challenge is to provide adequate performance for (possibly) heterogeneous traffic

## Slide 29: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 30: Error Control
Error control repairs frames that are received in error
  Requires errors to be detected at the receiver
  Typically retransmit the unacknowledged frames
  Timer protects against lost acknowledgements
Detecting errors and retransmissions are next topics.
Notes: We’ll get to this later in the chapter (error detection/correction, and elementary data link protocols)

## Slide 31: Error detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 32: Error Detection – Parity (1)
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110000  11100001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 11100101; detected, sum is wrong
  Ex: 3 errors, 11011001; detected sum is wrong
  Ex: 2 errors, 11101101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½
Can be generalized to more errors detected (and corrected)

## Slide 33: Error Detection – Parity (2)
Interleaving of N parity bits detects burst errors up to N
  Each parity sum is made over non-adjacent bits
  An even burst of up to N errors will not cause it to fail

## Slide 34: Error Detection – Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: Internet 16-bit 1s complement checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors (with what probability?)
  Vulnerable to systematic errors, e.g., added zeros

## Slide 35: Cyclic redundancy check
more powerful error-detection coding
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 36: Error Detection – CRCs
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 37: Error Detection – CRCs
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors

## Slide 38: Error Detection and Correction
Codes’ structured redundancy allow some errors to be detected
Error detection codes:
  Parity »
  Checksums »
  Cyclic redundancy codes »
Structured redundancy can help correction of likely errors
Forward error correction codes:
  Hamming codes »
  Binary convolutional codes »
    Commonly used as inner codes
  Reed-Solomon and Low-Density Parity Check codes »
    Mathematically complex, widely used in space systems as outer codes

## Slide 39: Error Correction – Hamming code
Hamming code gives a simple way to add check bits and correct up to a (dmin-1)/2
  Check bits are parity over subsets of the codeword
  Recomputing the parity sums (syndrome) gives the position of the error to flip, or 0 if there is no error
(7, 4) Hamming code adds 3 check bits and can correct 1 error

## Slide 41
Computationally much more efficient!