## Slide 1: EXAMPLES

## Slide 2: Ethernet
“dominant” wired LAN technology:
single chip, multiple speeds (e.g., Broadcom BCM5761)
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 3: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (interfere with each other)
  sharing the channel
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 4: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 5: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 6: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 7: 802.3 Ethernet standards: link & physical layers
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 8: Wireless LANs
  802.11 architecture/protocol stack »
  802.11 physical layer »
  802.11 MAC »
  802.11 frames »

## Slide 9: 802.11 Architecture/Protocol Stack (1)
Wireless clients associate to a wired AP (Access Point)
  Called infrastructure mode; there is also ad-hoc mode with no AP, but that is rare.
Access Point
Client
To Network

## Slide 10: 802.11 Architecture/Protocol Stack (2)
MAC is used across different physical layers

## Slide 11: 802.11 physical layer
  NICs are compatible with multiple physical layers
    E.g., 802.11 a/b/g
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 12: 802.11 MAC (1)
  CSMA/CA inserts backoff slots to avoid collisions
  MAC uses ACKs/retransmissions for wireless errors

## Slide 13: 802.11 MAC (2)
Virtual channel sensing with the NAV and optional RTS/CTS (often not used) avoids hidden terminals

## Slide 14: 802.11 MAC (3)
  Different backoff slot times add quality of service
    Short intervals give preferred access, e.g., control, VoIP
  MAC has other mechanisms too, e.g., power save

## Slide 15: 802.11 Frames
  Frames vary depending on their type (Frame control)
  Data frames have 3 addresses to pass via APs

## Slide 16: Broadband Wireless
  802.16 Architecture / Protocol Stack »
  802.16 Physical Layer »
  802.16 MAC »
  802.16 Frames »

## Slide 17: 802.16 Architecture/Protocol Stack (1)
Wireless clients connect to a wired basestation (like 3G)

## Slide 18: 802.16 Architecture/Protocol Stack (2)
MAC is connection-oriented; IP is connectionless
  Convergence sublayer maps between the two

## Slide 19: 802.16 Physical Layer
Based on OFDM; base station gives mobiles bursts (subcarrier/time frame slots) for uplink and downlink

## Slide 20: 802.16 MAC
Connection-oriented with base station in control
  Clients request the bandwidth they need
Different kinds of service can be requested:
  Constant bit rate, e.g., uncompressed voice
  Real-time variable bit rate, e.g., video, Web
  Non-real-time variable bit rate, e.g., file download
  Best-effort for everything else

## Slide 21: 802.16 Frames
  Frames vary depending on their type
  Connection ID instead of source/dest addresses
(a) A generic frame. (b) A bandwidth request frame
(b)
(a)

## Slide 22: Bluetooth
  Bluetooth Architecture »
  Bluetooth Applications / Protocol »
  Bluetooth Radio / Link Layers »
  Bluetooth Frames »

## Slide 23: Bluetooth Architecture
Piconet master is connected to slave wireless devices
  Slaves may be asleep (parked) to save power
  Two piconets can be bridged into a scatternet

## Slide 24: Bluetooth Applications / Protocol Stack
Profiles give the set of protocols for a given application
  25 profiles, including headset, intercom, streaming audio, remote control, personal area network, …

## Slide 25: Bluetooth Radio / Link Layers
Radio layer
  Uses adaptive frequency hopping in 2.4 GHz band
Link layer
  TDM with timeslots for master and slaves
  Synchronous CO for periodic slots in each direction
  Asynchronous CL for packet-switched data
  Links undergo pairing (user confirms passkey/PIN) to authorize them before use

## Slide 26: Bluetooth Frames
Time is slotted; enhanced data rates send faster but for the same time; addresses are only 3 bits for 8 devices
(b)
(a)
(a)
(b)

## Slide 27: RFID
  Gen 2 Architecture »
  Gen 2 Physical Layer »
  Gen 2 Tag Identification Layer »
  Gen 2 Frames »

## Slide 28: Gen 2 Architecture
Reader signal powers tags; tags reply with backscatter

## Slide 29: Gen 2 Physical Layer
  Reader uses duration of on period to send 0/1
  Tag backscatters reader signal in pulses to send 0/1

## Slide 30: Gen 2 Tag Identification Layer
Reader sends query and sets slot structure
Tags reply (RN16) in a random slot; may collide
Reader asks one tag for its identifier (ACK)
Process continues until no tags are left

## Slide 31: Gen 2 Frames
  Reader frames vary depending on type (Command)
    Query shown below, has parameters and error detection
  Tag responses are simply data
    Reader sets timing and knows the expected format
Query message